## Slide 1
C A M E R A
ITEM | Fixed Lens IR Bullet Camera | Fixed Lens IR Bullet Camera | Fixed Lens IR Dome Camera | 
Housing |  |  |  | 
Model Name | ATC-A286FU-36W | ATC-A256FC-36W | ATC-A386FOI-36W | ATC-A356FOI-36W
Resolution | 2MP/1080P | 5MP | 2MP/1080P | 5MP
Effective Pixels | 1920x1080 | 2592x1520 | 1920x1080 | 2592x1520
ISP | NVP2470H | NVP2475H | NVP2470H | NVP2475H
Image Sensor | GC2023 1/2.7" CMOS | SC5035 1/3" CMOS | GC2023 1/2.7" CMOS | SC5035 1/3" CMOS
Frame Rate | PAL: 25fps / NTSC: 30fps | PAL: 25fps / NTSC: 30fps | PAL: 25fps / NTSC: 30fps | 
Lens | 3.6mm | 3.6mm | 3.6mm | 
Synchronization | Internal | Internal | Internal | 
Video Output (BNC | 1 Channel | 1 Channel | 1 Channel | 
Hybrid Output | TVI Only | TVI Only | TVI Only | TVI Only
Day & Night | IR cut filter with auto switch | IR cut filter with auto switch | IR cut filter with auto switch | 
IR LED | 12pcs SMD LEDs | 18pcs SMD LEDs | 18pcs SMD LEDs | 
LENS | 3.6mm |  |  | 
DNR | 3D | 2D | 3D | 2D
Power Consumption | Max 4.2W | Max 4.2W | Max 4.2W | 
Working Environment | -10°C~+55°C/ Less than 95%RH | -10°C~+55°C/ Less than 95%RH | -10°C~+55°C/ Less than 95%RH | 
Power Supply | DC12V±10% | DC12V±10% | DC12V±10% | 
Structure | Plastic | Metal | Plastic | 
Waterproof | IP66 | IP66 | IP66 |